## Slide 1
LIVE DEMONSTRATION · 6 MINUTES
LINE-1 Digital Twin
A production line that predicts its own failures — and explains them in plain language.
5
stations modelled
2 Hz
live telemetry
40 min
early warning
0
internet required
Step-by-step walkthrough · what to click, what to say, and what the numbers mean
Notes: Open the dashboard before this slide so it is already streaming. Confirm the header shows "Telemetry live" and a copilot provider. Leave the clock at 1x. Press Reset if anyone has been clicking around.

## Slide 2
THE PREMISE
Not a dashboard. A model of the plant you can drive.
1
It runs the physics
Five stations with real cycle times, a thermal model with a controller, tooling that wears, and finite buffers between machines that make them block and starve each other.
2
It sees failure coming
A least-squares fit on recent data, projected to the alarm limit. In testing it warned at 2.8 mm/s against a 4.5 limit — 40 minutes before the threshold was crossed.
3
It explains itself
An LLM copilot reads the live telemetry and traces cause to effect. It is never told which fault was injected — the diagnosis comes from the data.
Notes: This is the framing slide. The three claims map onto the demo: step 2 proves the physics, step 4 proves the prediction, step 5 proves the explanation.

## Slide 3
THE ASSET
LINE-1 — assembly and cure, five stations
CONV-01
Infeed Conveyor
Belt speed
Motor current
cycle 4.0 s
CNC-02
Machining Centre
Bearing vibration
Spindle load, tool wear
cycle 4.4 s
OVN-03
Curing Oven
3 zone temps
Burner duty
cycle 4.2 s
INS-04
Vision Inspection
Reject rate
Camera confidence
cycle 3.6 s
PKG-05
Packer
Output rate
Film tension
cycle 4.1 s
CNC-02 is the constraint
Longest cycle at 4.4 s, so line output tracks it directly. It is also where the demo fault lives — which is why the fault matters.
Buffers of 8 between stations
Machines block and starve each other. Stop the packer and work in progress backs up until the whole line is blocked — visible in the 3D view as product piling up.
Notes: Do not dwell here. One sentence per station at most. The point to land is that CNC-02 is the bottleneck, because that is why the bearing fault costs output.

## Slide 4
ARCHITECTURE
One seam. Everything above it is source-agnostic.
Telemetry sources
Simulated line (today)
MQTT / Sparkplug B
OPC-UA from PLC or SCADA
Historian or CSV replay
Twin core
Threshold alarms + latching
Learned, frozen baselines
Least-squares trend projection
OEE with loss attribution
Interfaces
3D line view
Trend charts + alarm feed
What-if setpoints and faults
LLM copilot
What this buys you
Connecting your plant means implementing one class — the analytics, the alarms, the dashboard and the copilot need no changes at all. That is why "can it take our data?" is a day of work rather than a rebuild.
Notes: If the customer has an integration architect in the room, this is the slide they came for. Offer docs/architecture.md as a follow-up — it names the four things that bite: staleness, status codes, source timestamps, and unit conversion.

## Slide 5
RUN OF SHOW
Seven steps, six minutes, one story
1
Baseline
0:00
A well-run line having a normal day. 87% OEE.
2
Prove it is a model
0:45
Change a setpoint, watch physics respond.
3
Inject the fault
1:45
Start a bearing degrading. Compress time 60x.
4
The prediction
2:30
Warned 40 min before the limit is crossed.
5
The copilot explains
3:30
Traces vibration to wear to rejects to OEE.
6
Intervene and recover
5:00
Replace the bearing. Watch OEE come back.
7
The credibility close
5:45
Same answer with the AI switched off.
Notes: Resist showing every feature. There are four injectable faults; the demo uses one. The other three exist to answer "what else can it do?" — mention, do not fire.

## Slide 6
1
Baseline — a normal day
0:00 · 45 seconds
87.4
%
OEE · rolling 20 minutes
100%
Availability
91%
Performance
97.6%
Quality
SAY THIS
"OEE is 87%. Availability is 100% — nothing has broken down. Performance is 91%, and that's micro-stops. Quality is 97.6%. That's a well-run line having a normal day."
DO THIS
Orbit the 3D view once, slowly
Click CNC-02 in the 3D scene — the charts below follow it
Point at the OEE tile and its three factors
Why this beat matters
The baseline has to be believable before the failure means anything. A line reading 100% is a line nobody trusts — micro-stops and unplanned stops are modelled, so 87% arrives for reasons you can name. If they accept this number, they accept everything after it.
Measured on a pre-warmed line, mean of 8 simulator seeds. World-class OEE is ~85%; a typical plant is 60–75%.
Notes: If asked why not 100%: micro-stops are the single largest OEE loss in most real plants, and they are modelled here rather than hardcoded. Performance is capped at 100% by definition, so buffer draining can never produce an OEE above 100%.

## Slide 7
2
Prove it is a model, not a dashboard
0:45 · 60 seconds
Chart: Oven setpoint 305 → 330 °C: measured response
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60
Zone 2 temp (°C) | 305.2 | 309.4 | 316 | 321.7 | 325.6 | 328 | 329.1 | 329.8 | 330.3 | 330.5 | 330.5 | 330.4 | 330.7
10 s
only 44% of the way there
30 s
within 1 °C of setpoint
68 → 85 → 74%
burner duty overshoots, then settles
SAY THIS
"It doesn't jump. Ten seconds in it's only 44% of the way there, and it settles in about half a minute. Look at burner duty — it spikes to 85% then settles at 74% as the controller finds the new equilibrium. That's a thermal model with a controller on top. A dashboard would just redraw a number."
DO THIS
Drag Oven setpoint: 305 → 330 °C
Point at Zone temperatures, then at Burner duty
Drag it back to 305 °C
Single measured run, seed 1. First-order thermal lag per zone with a PID on burner duty.
Notes: This is the slide that separates a twin from a dashboard, and it is the one people underrate. Do not rush it. The burner duty overshoot is the detail that convinces control engineers.

## Slide 8
3
Inject the fault, compress time
1:45 · 45 seconds
CNC-02 bearing degradation
Spindle bearing begins to spall. Vibration rises exponentially, spindle load creeps up, tooling wears faster, and out-of-tolerance parts start reaching inspection.
Progressive by design — a real bearing does not fail the instant you press a button, and the whole point is watching it develop.
Why 60×
In a real plant this plays out over days. At 60× it plays out in about thirty seconds — the clock is the only thing sped up; the physics is unchanged.
Say the 60× out loud and point at the sim clock. Never let the room think this is real time.
DO THIS
What-if controls → Inject on "CNC-02 bearing degradation"
Set the clock to 60×
Watch Bearing Vibration climb toward the dashed Warn 3.5 line
SAY THIS
"I've just started a spindle bearing degrading. In a real plant this plays out over days — I'm running the clock at 60×, so we'll watch it in about thirty seconds. Everything else stays physical. The clock is the only thing I sped up."
Notes: Injecting the fault is logged separately from the telemetry, so the copilot never sees which fault you chose. Mention that here — it sets up step 5.

## Slide 9
4
The prediction — the money shot
2:30 · 60 seconds
Chart: Vibration after fault onset — warned at 2.8, limit is 4.5
| 0 | 2.5 | 5 | 7.5 | 10 | 12.5 | 15 | 17.5 | 20 | 22.5 | 25 | 27.5 | 30
Bearing vibration (mm/s RMS) | 1.67 | 1.89 | 1.99 | 2.36 | 2.78 | 3.43 | 4.23 | 4.85 | 4.88 | 4.86 | 4.79 | 4.74 | 4.79
Warn 3.5
Alarm 4.5
40 min
of warning, while the machine still looked fine
Fired at 10 min, with vibration at 2.79 mm/s — well under the 4.5 alarm limit.
Fired in 8 of 8 test seeds.
SAY THIS
"Nothing is over limit yet — but it's telling me I hit the 4.5 alarm limit in about 40 minutes of run time. It's a least-squares fit over the last twenty minutes, extrapolated to the limit, and it only reports when the fit is good enough to mean anything. It's a regression, not a black box. I can show you the arithmetic."
Do NOT call this AI
Calling a straight-line fit "AI prediction" is the fastest way to lose the engineer in the room. The AI story is the copilot.
Mean of 8 simulator seeds. Projection suppressed when the fit quality r² falls below 0.55 — no projection is shown rather than a bad one.
Notes: Someone always asks how it predicts. The answer is one sentence: least-squares fit over recent run time, projected to the threshold, suppressed when r-squared is too low to trust. Offer to open server/analytics/trend.js.

## Slide 10
5
The copilot explains itself
3:30 · 90 seconds
COPILOT · reading live telemetry
CNC-02 is running, but it is carrying two active alarms: Bearing vibration: 4.97 mm/s RMS, above the 4.5 mm/s alarm limit. That is the measurement; the likely inference is a degrading spindle bearing. High vibration accelerates tool wear (climbing 0.34%/min, r²=1.00) and both push parts out of tolerance — consistent with INS-04 reject rate at 5.45%, above its 4% warning limit.
It was not told
Fault-injection events are filtered out of its context. The diagnosis is earned from telemetry.
Measurement vs inference
Verbatim: "That is the measurement; the likely inference is..."
It traces the chain
Vibration → tool wear → out-of-tolerance parts → reject rate → OEE.
DO THIS
Click "Explain this" on the bearing alarm
While it thinks: say it is not told which fault you injected
Then click the "Draft a maintenance work order" chip
Latency warning
Use the Local model for this beat. Cloud can take 30 s to start talking.
Verbatim excerpt from a live run. Model: stealth/ox-alpha via OpenRouter.
Notes: Read the answer out loud rather than letting them read it. Emphasise the causal chain — that is what a dashboard cannot do. Then the work order, because that is the operational payoff: it goes to their CMMS.

## Slide 11
6
Intervene, and watch it recover
5:00 · 45 seconds
Chart: OEE with the fault vs an identical control line
| 0 | 2.5 | 5 | 7.5 | 10 | 12.5 | 15 | 17.5 | 20 | 22.5 | 25 | 27.5 | 30
Fault left unaddressed | 87.4 | 86.7 | 86.7 | 86.7 | 86.4 | 86.4 | 85.6 | 82.8 | 79.7 | 78.2 | 76 | 72.7 | 69.8
Identical line, no fault (control) | 87.4 | 86.7 | 86.7 | 86.7 | 86.5 | 86.5 | 86.6 | 86.7 | 86.6 | 87.6 | 88 | 88.6 | 88.1
17.6
OEE points lost in 30 min
2.3×
reject rate, 2.2% → 5.2%
Why a control line matters
The green line is the same simulator, same seed, no fault. It holds 88%. That is what proves the drop is the fault and not ordinary variation — the question an analyst will ask, answered before they ask it.
DO THIS
Clear the bearing fault, then click Tool change
Set the clock to 20×
Watch reject rate fall and OEE climb back
SAY THIS
"Bearing replaced, fresh tooling. The twin closed the loop — it found it, explained it, and now confirms the fix worked."
Mean of 8 paired simulator seeds; control and faulted lines share a seed, so the only difference is the fault.
Notes: This is the ROI slide in disguise. 17.6 OEE points on a real line is a large number — invite them to put their own throughput and margin against it.

## Slide 12
7
The credibility close
5:45 · 30 seconds
Switch the AI off. Ask again.
Set the copilot to "Offline rules" and ask "Why is OEE down?" again. The same diagnosis comes back — in 40 milliseconds, from a deterministic rule engine, with no model and no network involved.
Cloud
2–35 s
to first token
Best analysis. Variable.
Local
~1 s
to first token
The live walkthrough.
Offline rules
40 ms
to first token
Deterministic. Always.
SAY THIS
"Same conclusion, no model, no network. The AI makes it conversational — it isn't where the analysis comes from. Everything you just saw is a threshold, a regression, or an OEE calculation you can audit."
This move is worth more than it looks
It is the answer to "is the AI just making this up?" — and it lands far better as a demonstration than as a claim.
Then land it: "This runs on a simulated line today. The ingest layer is built to take your data — MQTT, OPC-UA or a historian export — and nothing above that layer changes when we swap it."
Notes: Ending on the rule engine rather than on the AI is deliberate. It inoculates against the "AI hallucinates" objection in the follow-up meeting, when you are not in the room to defend it.

## Slide 13
ANTICIPATING THE SCEPTIC
Six decisions that let this survive an engineer
87% not 100%
Micro-stops and unplanned stops are modelled. Performance is capped at 100% by definition, so buffer draining can never yield OEE above 100%.
Regression not "AI prediction"
Least-squares fit projected to the limit, suppressed when r² is too low to trust. Auditable arithmetic.
Blind copilot
Fault-injection events are filtered from its context. It diagnoses from telemetry.
Stale not zero
A dropped sensor holds its last value and flags itself. Charts stop rather than drawing a flat line that reads as healthy.
Coupled not random
Finite buffers make stations block and starve each other. Vibration drives wear drives rejects drives OEE.
Read-only by choice
OPC-UA could write setpoints to a PLC. It deliberately does not — that needs interlocks, an audit trail and your sign-off.
Every one of these is a decision you can defend out loud — which is the difference between a demo that closes and a demo that raises doubts.
Notes: You do not present this slide. It is here so that when a question comes, you have the answer in front of you.

## Slide 14
THE OBVIOUS QUESTION
"Can it take our data?"
MQTT / Sparkplug B
Map your topics to signals, implement one class. Sparkplug decodes metric aliases from NBIRTH/NDATA.
OPC-UA
Browse your address space, map NodeIds, subscribe. Honour StatusCode and prefer source timestamps.
Historian / CSV
Simplest first step: replay an export on a timer. Real customer data with no plant network access.
Four things that bite
Staleness — flag it, never render stale as live
Status codes — a Bad reading is not a data point
Timestamps — use source, not arrival time
Units — convert at the boundary, or every threshold is wrong
Everything above the ingest seam — analytics, alarms, dashboard, copilot — needs no changes at all. That is the difference between a day of integration work and a rebuild.
Both adapters ship as documented stubs with the real interface signatures. See docs/architecture.md.
Notes: Offer the architecture one-pager as the follow-up artefact. If they have a historian, push for the CSV replay first — it is real data in the twin without touching plant networks or waiting on IT.

## Slide 15
PRESENTER CHECKLIST
Ten minutes before you walk in
✓
Start it
npm run dev, open localhost:5173. Confirm "Telemetry live" in the header.
✓
Pick the model
AI ⚙ → choose a provider → Test. Under 4 s is presentable live.
✓
Reset the line
Press Reset. It re-warms to ~87% OEE, all clear, in under a second.
✓
Leave the clock at 1×
You speed it up in step 3, not before.
✓
Rehearse with wifi off
Once. The rule engine is your safety net — know what it looks like.
If something breaks
Disconnected → npm run dev again; it reconnects itself
Copilot silent → switch to Offline rules and carry on
Odd state → press Reset
3D choppy → drop the clock to 20×
Do not show everything
There are four injectable faults. The demo uses one. The other three exist so you can answer "what else can it do?" — mention them, do not fire them.
Notes: The single highest-value item here is testing the model latency on the demo machine, on the demo network. Cloud latency was measured between 2 and 36 seconds on consecutive identical calls.

## Slide 16
WHERE THIS GOES NEXT
Three ways to make this yours
1
Your line, our model
Swap the five generic stations for your actual process and cycle times. A day or two of modelling.
2
Your data, live
Point the ingest layer at a historian export first, then MQTT or OPC-UA. Nothing above the seam changes.
3
Your failure history
Trend extrapolation is deliberately simple. With real failure records behind it, the prediction gets considerably better.
Runs entirely on one laptop · no cloud dependency · no internet required
Notes: Close by asking which of the three they want first. The historian replay is usually the fastest path to a second meeting, because it needs no plant network access.